## Slide 1: Design for X

## Slide 2: Design for X…A Short List
Design for Manufacturability
Design for Ergonomics
Design for Safety
Design for Environment
Design for Reliability
Design for Serviceability
Design for Retirement

## Slide 3: Design for Ergonomics
Who (User analysis…demography…height, weight, gender,..)
How? (Task analysis)
Usability? (How effectively does the proposed solution work?)
Anthropometrics (Data from Military Standards)
User percentiles
Key parameters
User friendliness
User bandwidth (Flexibility)
Validation and testing

## Slide 4: Design for Ergonomics
Ease of use for a large spectrum of employees (Height, weight, flexibility, etc.)
Dexterity
Vision (Lightings…Lumen, orientation, location,..)
Ease of Use (Grip, fatigue, ease of operation, etc.)
Fail safe design (In case of failure…..)
Standardization (Uniformity & avoidance of confusion)

## Slide 5: Design for Manufacturability & Processability
Material selection (Avoid regulated/restricted material)
Shape & Size
Ease of Manufacturing
Avoiding failures (Frequent & catastrophic)
Tolerances
Minimize secondary operations

## Slide 6: Typical DfM Design Rules
Space holes to be made in one operation without tooling weakness
Avoid generalized statements on drawings, i.e. “Polish this surface.”
Dimension from specific surfaces or points on the part
Dimension from a single datum to avoid tolerance stack-up
Design for minimum weight, within the strength and stiffness constraints
Whenever possible design to use general-purpose tooling
Use generous fillets and radii on castings, molded, formed and machined parts
Minimize the number of separate operations and set-u

## Slide 7: Design for Manufacturability (Continued)
Stress Material Uniformly!
Bending: Inefficient – Often only 1% of material carrying the max stress
Tension: Great! – Often 99% of material sharing the mean stress
Torsion: OK

## Slide 8: Summary of DfA (Assembly)
Design with the minimum number of parts
Develop a modular design
Minimize part variations
Design parts to be multifunctional
Design parts for multiuse
Design parts for ease of fabrication
Avoid separate fasteners
Minimize assembly directions; top-down assembly
Maximize compliance, ease of assembly
Minimize handling; DF handling and presentation
Evaluate assembly methods
Eliminate or simplify adjustments
Avoid flexible components

## Slide 9: Design for Safety
Material
Ergonomic features
Safety features and signs
Fail Safe Design
Add protective devices
Use EPA and OSHA approved paints & materials

## Slide 14: Inherently Safe Design
Use safer materials by substitution (Water rather detergent)
Minimize hazardous materials & ensure to contain them properly
Use proper signs & switches (Kill Switches)
Use sensors and controls to accommodate accidental overload
Use Adequate Safety Factor in your Design
Simpler the Design Safer & More Reliable is the Design

## Slide 15: Fail Safe Design
Cannot operate a Microwave oven IF the door is open!
Forcespinning [TM] cannot operated IF the All the Safety Features are Not in place
Circuit Breakers

## Slide 16: Design for Environment
Material (Recycled, recyclable or Biodegradable materials)
Maximize life expectancy
Improve disposability (Redesign packaging if possible)
Improve serviceability/repairability