## Slide 1: Homeostatic environment chamber
Essential Conditions:
Formulation of Parameters
  CO2: 5% ± 0.1%
  pH: 7.4% ± 0.04%
  Temperature: 37°C ± 2°C
  Humidity: 95% ± 0.01%
Source: DSS Imagetech
Homeostatic Environment Chamber Placed on Stage Top of Microscope

## Slide 2: CONCEPTUAL DESIGN
Homeostatic Environment Chamber
pH Sensor
Humidity Sensor
CO2 Sensor
Temperature Sensor
Controller

## Slide 3: Functional decomposition
Chamber
Sensors
Control System
Source
Display System

## Slide 4: Concept generation
Function | Sub-Function | 
Chamber | Lid CO2 Valve Water Inlet Insulation | Plexiglass Windows (Top/Bottom) Gasket
Sensors | Temperature CO2 | pH Humidity
Control System | Temperature Controller CO2 Controller | Microcontroller Data Collecting Output
Source | Power On/Off | Peltier Coolant
Display System | Temperature CO2 | pH Humidity

## Slide 5: Sub-sub function of controller
Temperature Controller Block Diagram

## Slide 6: Design criteria
Sensitivity
Range
Accuracy
Cost
Design Criteria Temperature Sensors
Weighting Matrix | Sensitivity | Range | Accuracy | Cost | Score = Row Sum | Weight.
Sensitivity | X | 5 | 3 | 1 | 9 | 0.25
Range | 1 | X | 1 | 1 | 3 | 0.08
Accuracy | 3 | 5 | X | 3 | 11 | 0.31
Cost | 3 | 5 | 5 | X | 13 | 0.36
Total number of comparisons = Sum of Scores |  |  |  |  | 36 | 1

## Slide 7: CONCEPT VARIANTS
Concept Variance Ranking With Respect To Sensitivity
Concept Variance Ranking With Respect To Range
Sensitivity | Thermocouple | RTD | Thermistor | Score = Row Sum | Normal Score
Thermocouple | X | 3 | 1 | 4 | 0.22
RTD | 3 | X | 1 | 4 | 0.22
Thermistor | 5 | 5 | X | 10 | 0.56
Column Sum | 8 | 8 | 2 | 18 | 1
Range | Thermocouple | RTD | Thermistor | Score = Row Sum | Normal Score
Thermocouple | X | 2 | 1 | 3 | 0.17
RTD | 4 | X | 1 | 5 | 0.28
Thermistor | 5 | 5 | X | 10 | 0.56
Column Sum | 9 | 7 | 2 | 18 | 1

## Slide 8: Concept variants
Concept Variance With Respect To Accuracy
Concept Variance With Respect To Cost
Accuracy | Thermocouple | RTD | Thermistor | Score = Row Sum | Normal Score
Thermocouple | X | 1 | 3 | 4 | 0.22
RTD | 5 | X | 3 | 8 | 0.44
Thermistor | 3 | 3 | X | 6 | 0.33
Column Sum | 8 | 4 | 6 | 18 | 1
Cost | Thermocouple | RTD | Thermistor | Score = Row Sum | Normal Score
Thermocouple | X | 3 | 3 | 6 | 0.33
RTD | 3 | X | 1 | 4 | 0.22
Thermistor | 3 | 5 | X | 8 | 0.44
Column Sum | 6 | 8 | 4 | 18 | 1

## Slide 9: Selection process
-100°C to 150°C
Negative Temperature Coefficient
Highly Sensitive
59¢
Thermistor is the Winner!
Selection Process of Temperature Sensors
 | Sensitivity | Range | Accuracy | Cost | Score
Thermocouple | 0.05 | 0.01 | 0.07 | 0.12 | 0.26
RTD | 0.05 | 0.07 | 0.14 | 0.08 | 0.34
Thermistor | 0.14 | 0.05 | 0.10 | 0.16 | 0.45

## Slide 10: drawings
208mm x 110mm x 25mm