## Slide 1: A GIS-Based Model to Assess Onsite Sewage Facility (OSSF) Contamination Risk to Local Water Resources
By Alvaro Garcia

## Slide 2: What is an On-Site Sewage Facility?
  Decentralized wastewater treatment systems
  Efficiently treat wastewater through physical, chemical, and biological processes
  Cost effective especially for rural areas
  Rely on the proper design, installation, and management of the system
“A Conventional Septic System”
Source: EPA

## Slide 3: OSSF Potential Risks
  Public Health
    Bacterial exposure via public waterways
      Drainage ditches
      Resacas
      Groundwater
    Contact recreation in the Lower Laguna Madre
  Environment
    Nutrient discharge
    Eutrophication
Subwatershed Boundaries with Major Drainage Routes and Resacas (Benavides, LLM/Ship Channel Watershed Characterization, 2018)

## Slide 4: OSSF Potential Risks
  Public Health
    Bacterial exposure via public waterways
      Drainage ditches
      Resacas
      Groundwater
    Contact recreation in the Lower Laguna Madre
  Environment
    Nutrient discharge
    Eutrophication
LLM/Brownsville Ship Channel TCEQ Segments (Benavides, LLM/Ship Channel Watershed Characterization, 2018)

## Slide 5: Research Objectives
Develop a GIS risk assessment model that considers relevant OSSF risk parameters
Determine the relative importance between the risk model’s parameters
Evaluate the risk model’s performance using E. Coli counts.

## Slide 6
Geographic Information Systems (GIS)
Notes: Add Up and down arrow and side to side arrow

## Slide 7: OSSF Risk Assessment Model (Oosting and Joy, 2011)
  Environmental
    Soil Type
    Land Slope
    Floodplain
    Groundwater Recharge Areas
  OSSF System Design
    Lot Size
    Surface Water Proximity
    System Age
    Water Supply Proximity
    OSSF Density
250 m by 250 m survey grid generated in GIS

## Slide 8: OSSF Database
  OSSF records from Cameron County Public Health department were matched with appraisal district parcel maps and 911 addresses
  Around 10,000 permits were automatically matched
  Remaining permits are being manually matched using physical permit copies
OSSF locations of automatically matched permits.
Source: Texas Water Resource Institute & Texas A&M Agrilife Extension Service

## Slide 9: Environmental Parameters
  Soil Type
    Class A and Class D = 5
    Class B = 3
    Class C = 1
  Land Slope
    < 5% = 1
    5-10% = 2
    10-15% = 3
    15-20% = 4
    >20% = 5
  Floodplain
    Within = 5
    Outside = 1
  Groundwater Recharge Areas
    Within = 5
    Outside = 1

## Slide 10: System Design Parameters
  Lot Size
    >1 acre = 1
    0.75 - 1 acre = 2
    0.50 – 0.75 acres = 3
    0.25 – 0.50 acres = 4
    <= 0.25 acres = 5
  Surface Water Proximity
    Within 150 ft. = 5
    150 - 225 ft. = 4
    225 - 300 ft. = 3
    300 - 375 ft. = 2
    Beyond 375 ft. = 1

## Slide 11: System Design Parameters
  System Age
    <10 years = 1
    10-20 years = 2
    20-25 years = 3
    25-30 years = 4
    >30 years = 5
  Water Supply Proximity
    Within 300 ft. = 5
    300 – 450 ft. = 4
    450 ft. – 600 ft. = 3
    600 ft. – 750 ft. = 2
    Beyond 750 ft. = 1

## Slide 12: System Design Parameters
  Test Grid  Value  Risk Designation
  OSSF Density
    0-1 = 1
    2-4 = 2
    5-9 = 3
    10-16 = 4
    17-37 = 5

## Slide 13: Questions