## Slide 1
Implementation of Whole Body Scanner for
Real Time Optimization of Workstations
Faculty Advisor: Dr. Gonzalez
Course Advisor: Dr. Sarkar
Caleb Jaime
Manufacturing Engr.
Jesus G. Cavazos
Manufacturing Engr.
Estefania Gonzalez
Manufacturing Engr.

## Slide 2
  Outline
Background
Problem Formulation
  Problem Definition
  Background Research
  Goals, Objectives and Constraints
  QFD
Final Design
  Concept Generation Methodology
  Final Design
Manufacturing Processes
  BoM
  Process routing and Assembly
  Final Product
  Final Product Vs. CAD Model
  Operations Manual
  Maintenance Manual
Test Results and Analysis
  Raw Data
  Data Analysis
  Tables and graph
  Videos (during Experiments)
Results and Discussions
Conclusions
Best Practices
Lessons learned
Summary
Future Recommendations
References
Acknowledgements
Prototype Demonstration

## Slide 3: Problem Formulation
Industrial workstations generally designed for the extremes
  Ergonomic issues
    Unexpected costs
      Loss in productivity
      Increased levels of scrap
      Health claims

## Slide 4
Competitive Products

## Slide 5: Competitive Products cont.
Figure 1: Production Basics
Figure 2:
IAC Industries
Figure 3: LTW
$4,446
$3,228
$1,283

## Slide 6: Goals

## Slide 7: Objectives
Design and create a workstation 64”H*43L”*27”W made of steel and wood.
Create database to store body measurements and input in Arduino program.
Increase productivity by 10-15% ($500k-750k opportunity with 5M in sales)
Reduce overall cost by eliminating health and safety issues such as Musculoskeletal disorder (MSD): $32,000.00.

## Slide 8: Constraints (Design, Project & Customer)
Design Constraints
  Comply with 5’s (reduce waste and optimize productivity)
    Sort, Set in order, Shine, Standardize, Sustain
  Flexible for operators
  Safety!
Project Constraints
  3 Months for Design Development
  9 Months for Completion
  300 USD
Customer Constraints
  Cost effective & Reliable

## Slide 9: Quality Function Deployment

## Slide 10
 | Our Company | Production Basics
Feature 1 | Adjust height & angle electrically | Electric Height
Feature 2 | 500 Lummens (adjustable) | Not adjustable
Feature 3 | 12’’x7’’ foot rest | Foot Rest
Feature 4 | 65’’x43’’x27’’ | 36’’X48’’
Feature 5 | 200 lbs lift capacity | 125 lbs
Feature 6 | 15 s displacement | N/A
Feature 7 | HD Steel | Aluminum Legs
Cost | $3,500 (Target) | $3,228
Competitive Products
Market Opportunity: $25,000,000

## Slide 11: Functional Decomposition

## Slide 12: Selection Process
How did you identify key components?
Competitive products? Brain Storming? Combination?

## Slide 13
Concept Generation Results

## Slide 14: Final Design
Light Fixture
Wooden Foot Rest
Actuators
Wooden Table Top
Cork sheet

## Slide 15: Drawings
65 in
43 in
27 in

## Slide 16: BOM/Budget

## Slide 17: Prototype Vs. Production Cost
Cost of Materials: | Material | Quantiy | Price | Total
 | Square Tubing 2'' (40 ft.) | 2 | 68 | 136
 | Hardwood (worktable) 1ft^2 | 9 | 2.5 | 22.5
 | Actuators | 4 | 50 | 200
 | Arduino Board | 1 | 13.8 | 13.8
 | Cork Sheet for Back | 1 | 60 | 60
 | Ultrasonic Sensors | 5 | 8.99 | 8.99
 | LED Fixture | 1 | 70 | 70
 | Arduino Cables | 40 | 3.89 | 3.89
 | Arduino Dsiplay | 1 | 21.88 | 21.88
 | Relay Board | 1 | 6.25 | 6.25
 | Light Sensor | 1 | 5.55 | 5.55
 |  |  | Total: | 548.86
Cost of Materials: | Material | Quantity | Price | Total
 | Square Tubing 2'' (40 ft.) | 2 | 55 | 110
 | Hardwood (worktable) 1ft^2 | 9 | 2 | 18
 | Actuators | 4 | 40 | 160
 | Arduino Board | 1 | 10 | 10
 | Cork Sheet for Back | 1 | 55 | 55
 | Ultrasonic Sensors | 5 | 5 | 25
 | LED Fixture | 1 | 55 | 55
 | Arduino Cables | 40 | 2.5 | 2.5
 | Arduino Dsiplay | 1 | 15 | 15
 | Relay Board | 1 | 4 | 4
 | Light Sensor | 1 | 3.5 | 3.5
 |  |  | Total: | 458

## Slide 18: Assembly

## Slide 19: Prototype Building
Arduino Board
Relay
The numbers where the cables are connected in the board represent the pin output
Figure 4 Connection for Relay
Figure 3 Size Relation
Figure 5 Code for Pistons
Figure 2 Connection for H-Bridge
Arduino Board
H-Bridge
Connections for:
Ground
5V
12V
Cables indicate where to connect from the Arduino board to the H-Bridge
Figure 1 Painting of Workstation

## Slide 20: Final Design
Light Fixture
Wooden Foot Rest
Actuators
Wooden Table Top
Cork sheet
Placement for Arduino
Actuators
Cork sheet
Foot Rest

## Slide 21: Ergonomic Measurements
National Institute of Occupational Safety and Health (NIOSH)
  Precision Work
    1-4in above elbow height
  Light Work
    Just below elbow height
  Heavy Work
    4-6in below elbow height
    Actual reference?

## Slide 22: Data Collection
#
Height

## Slide 23: Test Trials - Precision
Ergonomically Correct
Ergonomically Incorrect

## Slide 24: Operator #1-Precision Work
Chart: Time to Complete a Task
| 1 | 2 | 3 | 4
Ergonomically Correct | 20.08 | 17.5 | 16.11 | 15.71
36'' (bending) | 22.61 | 21.31 | 19.7 | 19.23
36'' (Not Bending) | 60.02 | 39.8 | 31.53 | 30.61

## Slide 25: Operator #2-Precision Work
 | 11 Hr. Shift | 
 | Ergonomically Correct | Ergonomically Incorrect
Parts | 2112 | 1200
Parts Difference |  | 912
Lost production |  | 43%

## Slide 26: Operator #3-Precision Work
 | 11 Hr. Shift | 
 | Ergonomically Correct | Ergonomically Incorrect
Parts | 2880 | 2170
Parts Difference |  | 710
Lost production |  | 25%

## Slide 27: Precision Task Average
 | 11 Hr. Shift | 
 | Ergonomically Correct | Ergonomically Incorrect
Parts | 2408 | 1642
Parts Difference |  | 766
Lost production |  | 32%
 | Ergonomically Correct | Ergonomically Incorrect
Average (Time in Sec) | 16 | 24

## Slide 28: Test Trial 2- Heavy Work
Ergonomically Correct
Ergonomically Incorrect

## Slide 29: Operator #1- Heavy Work
 | 11 Hr. Shift | 
 | Ergonomically Incorrect | Ergonomically Correct
Parts | 709 | 932
Parts Difference | 224 | 
Lost Production | 24% | 

## Slide 30: Operator #2- Heavy Work
 | 11 Hr. Shift | 
 | Ergonomically Incorrect | Ergonomically Correct
Parts | 757 | 1025
Parts Difference | 268 | 
Lost Production | 26% | 

## Slide 31: Operator #3- Heavy Work
 | 11 Hr. Shift | 
 | Ergonomically Incorrect | Ergonomically Correct
Parts | 771 | 986
Parts Difference | 215 | 
Lost Production | 22% | 

## Slide 32: Heavy Task Summary

## Slide 33: Overall Results
Figure 3 shows time it takes for actuator to reach specified distance
Figure 1 shows overall results based on precision task
Figure 2 shows overall results based on precision task

## Slide 34: ROI

## Slide 35
Ergonomic workstation
  Increase productivity 10-15%
    Increase $500,000-750,000 gross profit
    Based on our studies 33% of loss in production!
  $25,000,000 Market Opportunity!
  Comply with 5’s
  Reliable, Capable, Profitable
Summary

## Slide 36: Thank you

## Slide 37: Operations Manual

## Slide 38: Maintenance Manual

## Slide 39
Gantt Chart