## Slide 1: Biomechanical Energy Harvester for Health Monitoring
Faculty Advisors: Dr. Caruntu & Dr. Fuentes
Course Advisor: Dr. Sarkar
Ezequiel Juarez
Christian Quintero
Bonifacio Salinas
Jaime Sifuentes

## Slide 2: Outline
Overview
  Elevator Speech
  Background Research
  Competitive Products
Final Design
  QFD
  Problem Definition
  Functional Decomposition
  Final Design
  Circuit Design
Market Analysis
  Prototype/Production Cost
Manufacturing Process
  Bill of Materials
  Assembly
Test Protocol
  Moment of Inertia
  LabVIEW
  Running &Walking
Results & Data Analysis
Summary

## Slide 3: Overview

## Slide 4: Elevator Speech
Health Monitoring Systems (H.M.S) currently limited by batteries
Bio-Mechanical Energy (B.M.E) = alternative source of power
B.M.E. + H.M.S. = New Opportunity
Impact: Health and Environment
  Diabetes
    26% of adults 65 and older
    Over 6 million increase form 2010 to 2012
    7th leading cause of death
    76,000 people in Rio Grande Valley
  Environment
    Environmentally friendly
    Minimize waste

## Slide 5: Background Research
Market Size: 1 in 10 adults.
  24 million fitness tracker users.
Average price:
  $140
Total Market Value:
  $3.4 Billion
Projected Market Capture:
  5%
Actual Market Value:
  $170 Million

## Slide 6: Competitive Products
5.
1.
2.
4.
3.
1
2
3
4
5

## Slide 7: Final Design

## Slide 8: Quality Function Deployment

## Slide 9: Needs Wants
Portable (<120g)
Comfortable (all day use)
Health/Fitness Monitor
Battery Life Extension
Heart Rate
Aesthetically appealing
Pedometer
Self-Powering
Objectives Constraints
Target Efficiency > 2%
Comfort (Full day)
Size (2.75"x0.8" )
Weight (<120g)
Cost ($100)
Increase efficiency
Decrease size/Weight < 120g
Cost Under $100
Health Monitoring Device
Problem Definition

## Slide 10: Functional Decomposition
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr
Sales | 1 | 1 | 1
Health Monitor
Generator
Battery

## Slide 11: Sub-Function 1- Selection
Health Monitor Decision |  |  |  | 
 | Dimension | Cost | Power | Score
Mio | 0.049 | 0.222 | 0.197 | 0.469
ePulse2 | 0.012 | 0.049 | 0.197 | 0.259
GlobalSat | 0.049 | 0.172 | 0.049 | 0.271
Battery Voltage: 3.7 V
Battery Life: 13 Hrs.
Power Consumption: 86 mW

## Slide 12: Sub-Function 2- Selection
Battery |  |  |  | 
 | Dimension | Cost | Capacity | Score
LIR | 0.148 | 0.074 | 0.185 | 0.407*
PCBM | 0.074 | 0.037 | 0.074 | 0.185
VL | 0.222 | 0.111 | 0.074 | 0.407
*Capacity / Cost Ratio WINNER!
Volts: 3.6 V
Capacity: 300 mAh
Diameter 30 mm
Weight: 7.3 g
Price: $ 9.50

## Slide 13: Sub-Function 3- Selection
Generator |  |  |  | 
 | Dimension | Weight | Power | Total
SONGLE | 0.056 | 0.167 | 0.111 | 0.334
NIDEC | 0.028 | 0.25 | 0.167 | 0.445
MINI | 0.084 | 0.084 | 0.056 | 0.223
Step angle 18°
Step angle tolerance 0.3°
Holding torque at Un 0.15cNm
Direction of rotation reversible
Electrical data
Drive Method 2-2 PHASE
Number of windings 2/4
Rated voltage Un 5V
Current /phase 500mA
External dimensions Φ15X11mm

## Slide 14: Final Design
All measurements are in inches.

## Slide 15: Comparison
Dimensions in inches

## Slide 16: Circuit

## Slide 17: Market Analysis

## Slide 18: Prototype Cost
Material Cost
  $60
Estimated Labor Cost (4 Hours @$40/Hour)
  $160
  Total Prototype Cost: $220

## Slide 19: Production Cost
Material Cost
  $ 8 per unit (not including health monitor)
Number of Labors
  25 for assembly and 5 engineer
  100,000 units per year
Labor Cost
  $18 per unit with 30% benefits
Estimated Production Cost
  $32 per unit with 20% overhead
  $62 per unit including HM
Distributor / Wholesale Price (30% Profit)
  $80 per unit including HM

## Slide 20: Market Analysis
Distributor Cost $80
Retail Price $105
  30% Profit
Target QFD Price $90
Market Size: $10.5 Million
Competitive price $100-$200

## Slide 21: Manufacturing Process

## Slide 22: Manufacturing Process for Prototype
Create plastic parts using 3D printing process
  1 – Case
  2 &3– Pendulum
Press-fit bearing (4) to case(1)
Epoxy large gear (5) to case (1)
Press fit shaft (6) into the bearing (4)
Super glue small gear (7) to generator (8)
Adhere generator (5) to pendulum (2&3)
Mount tungsten weights (9) on pendulum
Press fit pendulum (2&3) on to shaft (6)
Wire generator (5) phases onto bridge rectifier
6
7
5
3
4
2
1
8
9

## Slide 23: Bill Of Materials - Prototype
Material | Qty | Provider | PPU | Total
Spur Gear 70T 64P | 1 | World of RC Parts | 5.75 | 5.75
Spur Gear 10T 64P | 1 | VRC Hobbies | 2.49 | 2.49
Sankyo A55 Motor | 1 | China | 2.69 | 2.69
MB6S Rectifier | 2 | Mouser | 0.4 | 0.8
Joule Thief | 1 | Greece | 5.25 | 5.25
Bearing | 1 | RC Bearings | 1.60 | 1.60
 |  |  | TOTAL | 19.96

## Slide 24: Manufacturing Process
3D Printing case – Using Makerbot
Test Fitting Strap
Press fit shaft into bearing

## Slide 25: 3D Print - Case
Decreased case size to shorten printing time.
Changed dimensions slightly to better fit parts.

## Slide 26: 3D Print – Pendulum Arm
Split pendulum design into 2 pieces.
  Improved ease of printing
  Decreased printing time

## Slide 27: Assembly
Fit bearing-shaft and 70T gear onto case.
Fit generator onto pendulum armature

## Slide 28: Assembly Continued
Affix pinion gear onto generator
Fit pendulum arm onto steel shaft

## Slide 29: Final Design
70 Tooth Gear
Pendulum
Generator
Case
Tungsten Weights

## Slide 30: Test Protocol

## Slide 31: Moment of Inertia
Center of mass – Length Arm
Period of Small Oscillation
Old Device
NEW 2 Device
NEW 1 Device
Old Device
Old J = 2.237 x 10-4 kg m2 NEW 1 J = 3.471 x 10-5 kg m2
NEW 2 J = 4.772 x 10-5 kg m2
 | L (m) | M (kg) | T (s)
OLD | 0.024 | 0.11413 | 0.573
NEW 1 | 0.0286 | 0.04214 | 0.338
NEW 2 | 0.0229 | 0.07314 | 0.339

## Slide 32: Labview

## Slide 33: Modeling
New Moment of Inertia Model

## Slide 34: Experiments
Experiment 1
Experiment 2
Experiment 3

## Slide 35: Testing Protocol - Walking
Walking Speed:
  2.5 mph
Test Duration:
  120 s
3 different tests:
  Power Generation
  NO Power Generation w/gears
  NO gear contact
3x 10s periods for data collecting

## Slide 36: Testing Protocol - Running
Running Speed:
  5 mph
Test Duration:
  120 s
3 different tests:
  Power Generation
  NO Power Generation w/gears
  NO gear contact
3x 10s periods for data collecting

## Slide 37: Results & Data Analysis

## Slide 38: MATLAB Code Sample

## Slide 39: Experimental Data (Running 5mph)

## Slide 40: Kinetic Energy for Running 5mph

## Slide 41: Kinetic and Electrical Energy
Average Energy (J) |  |  |  | 
 | Eavg1 | Eavg2 | Eavg3 | Eavg(elec)
Old J=2.2e-4 kg m2 | 0.02526 | 0.02396 | 0.0205 | 0.000579
New J=3.4e-5 kg m2 | 0.0065 | 0.001433 | 0.000854 | 0.00006978
New2 J=4.8e-5 kg m2 | 0.003267 | 0.003266 | 0.002067 | 0.0002
Eavg1- No Gear Contact Eavg2- Gear contact no gen. Eavg3- Power gen.

## Slide 42: Efficiency
Efficiency (%) |  |  | 
 | Ƞ1 | Ƞ2 | Ƞtotal
Old | 94.85 | 13.72 | 2.29
New | 22.05 | 8.92 | 1.07
New2 | ~100 | 36.73 | 6.12

## Slide 43: Summary
Available market for human generated power input for health monitoring
Compared to last year’s design:
  Doubled efficiency
  Smaller total dimensions and weight
  Ergonomic improvements
Further changes needed for improved electrical efficiency

## Slide 44: Future Recommendation
Research available generators
Mitigate electrical energy losses due to rectification
Can be achieved by using higher quality diodes
Improve energy generation while maintaining acceptable efficiency
Adjust pendulum design for mounting of weights

## Slide 45: Best Practices
Scheduling between group mates
Consulting alternative opinions
Accounting for lead times
Have a backup plan

## Slide 46: Lessons Learned
Project requires more electrical knowledge than expected
Previous circuit experience was limiting
Extended research on generators
Proactive approach i.e. professional mode vs. student mode

## Slide 47: References
http://www.cdc.gov/diabetes/statistics
http://www.nike.com/us/en_us/c/nikeplus-fuelband
http://www.fitbit.com/flex
https://jawbone.com/up
http://lark.com/products/lark-pro/features
http://fitness-trackers.findthebest.com/
http://endeavourpartners.net/assets/Wearables-and-the-Science-of-Human-Behavior-Change-EP4.pdf
http://www.roymech.co.uk/Useful_Tables/Drive/Gear_Efficiency.html
http://www.faculty.fairfield.edu/wdornfeld/ME312/ToothLoads04.pdf

## Slide 48: Questions

## Slide 49: Appendix