## Slide 1: Laboratory Safety and Hazard Communication
Environmental Health, Safety and Risk Management Laboratory Safety Program

## Slide 2: Course Outline
Background
Chemical information
Protecting yourself
Regulated waste disposal
Emergency response

## Slide 3: Required Training
All laboratory personnel are required to attend basic laboratory safety training through the Department of Environmental, Health Safety and Risk Management .
  Know how to access chemical-specific information.
  Be familiar with relevant emergency procedures
All laboratory personnel are required to attend Laboratory specific training through your respective department .
  Speak with your laboratory supervisor

## Slide 4: Background

## Slide 5: Compliance Objectives
Texas Hazard Communication Act (DSHS)
OSHA Laboratory Standard (OSHA)
Resource Conservation Recovery Act (RCRA)
Emergency Response
Help to ensure that you leave just has healthy as when you arrived!

## Slide 6: Your Rights under the Texas Hazard Communication Act (THCA)
Information on your chemical exposures
Receive training on chemical hazards
Access copies of SDS’s
Receive appropriate protective equipment (free of charge)
File complaints, assist inspectors, or testify against your employer

## Slide 7: Be familiar with the chemicals you are working with
“Don’t go home at night wondering if the headache you have is from the chemicals you were working with”

## Slide 8: What Questions Should I be asking?
What type of hazard is the chemical I am working with and where do I get this information?
Is the quantity I am working with represent an acute or chronic exposure?
What are the potential routes of exposure and how to I protect myself?
What do I do in the event of an emergency?
Notes: Routes of Entry
Inhalation - use fume hood
Absorption - use proper gloves and lab coat
Ingestion - don’t eat drink or apply cosmetics in lab

## Slide 9: What Type of Hazard is the chemical I am working with?

## Slide 10: What are Hazardous Materials
Hazardous materials are chemicals that have the potential to impact negatively on health
Effects that may result from exposure to hazardous substances include poisoning; irritation; chemical burns; sensitization; cancer; birth defects; and diseases of certain organs such as the skin, lungs, liver, kidneys and nervous system. The substance, nature and extent of the exposure will determine the severity of the health effects.
A wide range of chemicals are classified as hazardous and include: • solids; • powders; • liquids; • gases; • pure chemicals; • mixtures.

## Slide 11: Where Do I Get The Information ?
Global Harmonization Standard (GHS)
Chemical Label
Safety Data Sheets
  Internet (www.utrgv.edu/ehs)
  Call EHSRM (665-3690) (882-5934)
  The manufacturer or distributor
  Teaching Assistants (teaching laboratories)

## Slide 12: Globally Harmonized System of Classification and Labeling of Chemicals (GHS)
The Hazard Communication Standard (HCS) (29 CFR 1910.1200(g)), aligned with the GHS in 2012, requires that the chemical manufacturer, distributor, or importer provide Safety Data Sheets (SDSs) for each hazardous chemical to downstream users to communicate information on these hazards.
SDSs were formerly called Material Safety Data Sheets, or MSDSs. The information contained in the SDS is largely the same as the MSDS, except now the SDSs are required to be presented in a consistent, user-friendly, 16-section format.

## Slide 13: HCS Pictograms and Hazards
Health Hazard | Flame | Exclamation Mark
• Carcinogen • Mutagenicity • Reproductive Toxicity • Respiratory Sensitizer • Target Organ Toxicity • Aspiration Toxicity | • Flammables • Pyrophorics • Self-Heating • Emits Flammable Gas • Self-Reactives • Organic Peroxides | • Irritant (skin and eye) • Skin Sensitizer • Acute Toxicity (harmful) • Narcotic Effects • Respiratory Tract Irritant • Hazardous to Ozone Layer (Non Mandatory)
Gas Cylinder | Corrosion | Exploding Bomb
• Gases under Pressure | • Skin Corrosion/ burns • Eye Damage • Corrosive to Metals | • Explosives • Self-Reactives • Organic Peroxides
Flame over Circle | Environment (Non Mandatory) | Skull and Crossbones
• Oxidizers | • Aquatic Toxicity | • Acute Toxicity (fatal or toxic)
Notes: Instructor Notes:
There are nine pictograms under the GHS to convey the health, physical and environmental hazards. The final Hazard Communication Standard (HCS) requires eight of these pictograms, the exception being the environmental pictogram, as environmental hazards are not within OSHA's jurisdiction. The hazard pictograms and their corresponding hazards are shown on this slide.
Pont out the red borders and explain the reasoning.
Under the revised Hazard Communication Standard (HCS), pictograms must have red borders. OSHA believes that the use of the red frame will increase recognition and comprehensibility. Therefore, the red frame is required regardless of whether the shipment is domestic or international.
Will OSHA allow blank red borders?
A. The revised Hazard Communication Standard (HCS) requires that all red borders printed on the label have a symbol printed inside it. If OSHA were to allow blank red borders, workers may be confused about what they mean and concerned that some information is missing. OSHA has determined that prohibiting the use of blank red borders on labels is necessary to provide the maximum recognition and impact of warning labels and to ensure that users do not get desensitized to the warnings placed on labels.

## Slide 14: Safety Data Sheets
An SDS is a document that contains chemical hazard and safe handling information.
Public employers in Texas are required to keep a current Safety Data Sheet (SDS) for every hazardous chemical they have on site regardless of the quantity of the chemical.
The SDS must be readily available during each work-shift to public employees at each workplace and within three days of a written request.
A substitute (non-manufacturer-specific) SDS can be used if it is identical to the manufacturer-specific SDS both in identity and formulation of the hazardous chemical.

## Slide 15: Safety Data Sheet (SDS)

## Slide 16: Typical SDS. What is it?

## Slide 17: Safety Data Sheets (SDS) – Where do I get one ?
Internet (www.utrgv.edu/ehs) (quick links)
Call EHSRM (665-3690) (882-5934)
The manufacturer or distributor
Teaching Assistants (teaching laboratories)

## Slide 18: Chemical Label Information

## Slide 19: Secondary Labeling Requirements
Secondary containers must comply with GHS labeling requirements except when the following criteria are met:
  The material is used within the work shift of the individual who makes the transfer
  The worker who made the transfer is in the work area the entire time during use
  The container stays in within the work area and in the possession of the worker who filled the container
Free program available by contacting the EHSRM

## Slide 20: Flammable Liquids

## Slide 21: Is it an Acute or Chronic Hazard?
Toxicity is defined by the LD-50
  Acute
    High dose, short duration
  Chronic
    Low dose, long duration

## Slide 22: Toxicology
“The right dose differentiates a poison and a remedy.”
Paracelsus
LD50 (Watch for < 50 mg/kg)
LC50 (Watch for < 200 ppm)
OSHA Permissible Exposure Level (PEL)
  Time Weighted Average (TWA) ( 10 ppm)
  Short Term Exposure Level (STEL) (10 ppm)

## Slide 23
What are the routes of exposure? How do I protect
myself?

## Slide 24: Be Like a Canary in a Coal Mine
Coal miners used to carry highly sensitive canaries into the mines to alert them of any undetected poisonous gasses that may have been present.
Your body usually hints of danger before permanent damage is done.
Be your own canary in your workplac4e.
Be aware of your body.
If you feel dizzy or ill or develop rashes, a sore throat, etc. stop what you are doing and investigate the situation.
Beware of “the zone”
  You may get into your work so thoroughly you don’t realize that you’re hurting yourself.

## Slide 28: Administrative Controls -Good Employee Work Practices
No eating, drinking or applying cosmetics when working with hazardous chemicals
Always wash hands after working with hazardous chemicals
Proper Storage of chemicals
Proper Labeling
Reuse of a chemical bottle

## Slide 29: Routes of Exposure
Depending on the chemical and how it is used in the workplace, there are a number of ways it may enter the body. The major routes of exposure to hazardous substances are
  inhalation of vapors, fumes, dusts and mists;
  ingestion in to the body (e.g. unclean hands, contaminated food, smoking; and
  absorption in to the body through direct contact with the skin, eyes etc.

## Slide 30: Inhalation

## Slide 31: Inhalation
Caused by working in poorly ventilated areas.
  Solution: Work in a well-ventilated area or under a fume hood. Wear recommended PPE.
Respiratory System

## Slide 32: Particle Clearance
Translocation to the circulatory system or directly to epithelial cells

## Slide 33: Protecting Yourself from Inhalation Exposure
Ventilation
  Fume hood if applicable
  Adequate number of air exchanges
  Fresh air vs recirculated air
PPE
  N95
  Fitted respirator

## Slide 34: Localized Ventilation Fume Hood
Biosafety Cabinet
Fume Hood

## Slide 35: Fume Hood
May not be used for permanent storage.
May not be cluttered with objects.
Sash Guidelines:
  Do not block the sash with objects.
    The sash should be able to lower without any obstructions.
  Always close the sash when not in use. (~1” gap)
  Pull down the sash to 12” or less while in use so that you are protected while working.
  Confirm adequate face velocity
    80-150 linear feet per minute (lfpm)
  Require annual inspections.

## Slide 36: Fume Hood Configurations
Place equipment on stand
Lower sash
Place contaminant source as far back as possible

## Slide 37: Biosafety Cabinets are not Fume Hoods

## Slide 38: Building Wide
Air flow to the laboratory should be “negative” or moving from the hallway into laboratory.
  This will help ensure that contaminants remain inside the laboratory.
  May be tested using a thin strip of paper/tissue.
Report any HVAC or plumbing issues to EHSRM or Facilities
-Strong air flow from ceiling duct or noisy flow.
-Uncomfortable temperatures.
-Positive flow (into hallways).
-Strong chemical odors.
-Any odors of natural gas.
-Water leaks.

## Slide 39: Respirator Purpose
A respirator protects the user from harmful inhalation of toxic atmosphere hazards such as:
  Dusts, fogs, fumes, mists, gases, smokes, sprays, fibers or vapors
The primary objective shall be to prevent contamination from toxic vapors
Notes: A respirator is a device to protect the wearer from the inhalation of harmful atmospheres.
Before implementing a respiratory program, all efforts should first be made to engineer out the hazards either by providing ventilation or isolating source.
Respirators must be approved for the type and severity of conditions in which they are to be used

## Slide 40: Major types of respirators
Two Types:
Air Purifying
Atmosphere supplying respirators
Must be approved by NIOSH
Medical evaluation required
Notes: NIOSH : National institute of Occupational Safety and Health must approved all respirators.
Atmosphere supplying: Air supply is received from compressed air, oxygen tank or compressor driven air not from the atmosphere.

## Slide 41: Air Purifying
Dust Mask
Half Mask
Full Face
Hood Powered
Loose Fitting
Powered
Notes: Dust mask, Half Mask and Full Face respirators need to be test fitted to the user

## Slide 42: Atmosphere Supplying
Supplied Air Respirator
Abrasive Blasting
Continuous flow
Self Contained
Breathing Apparatus
(SCBA)
Notes: SCBA minimum service life 30 minutes

## Slide 43: Requirements: Fit Tested
Must be Fit Tested with same brand, model and size that will be used
Tested before first use
Note: Facial hair may not be permitted if employee will use a respirator that requires tight seal
Notes: Must also pass a qualitative fit test
Additional test should be conducted if any changes are noted, employee reports changes, or if a supervisor visually notes changes in employee condition or behavior
Not only facial hair but also any other conditions like corrective glasses, dentures, or any condition that interfere with with a tight seal of the respirator.

## Slide 44: Absorption

## Slide 46: Absorption
Caused by direct skin or eye contact.
  Solution: Wear gloves and protective clothing. Immediately rinse off any splashed chemicals or dust residue.
The Eye

## Slide 47: Protecting Yourself from Absorption Exposure
Cover exposed skin
Eye protection
Goggles for splash hazards
Gloves
Masks
X
X

## Slide 48: Gloves
Gloves must be worn to protect hands from exposure to hazardous materials. Glove selection should be based on an appropriate risk assessment. Alternatives to latex gloves should be available.
In addition, BSL-2 laboratory workers should:
  a. Change gloves when contaminated, glove integrity is compromised, or when otherwise necessary.
  b. Remove gloves and wash hands when work with hazardous materials has been completed and before leaving the laboratory.
  c. Do not wash or reuse disposable gloves. Dispose of used gloves with other contaminated laboratory waste. Hand washing protocols must be rigorously followed.

## Slide 49: Examples of Personal Protective Equipment (PPE)
Splash Goggles
Chemical Resistant Gloves
Laboratory Coat
Respirator
Face Shield
Temperature Resistant Gloves

## Slide 50: Personal Protective Equipment
Minimum Level of Personal Protective Equipment
  Closed Toed Shoes
  Long Pants
When working with chemicals
  Labcoat
  Safety Goggles (Prescription glasses are not safety goggles)
  Gloves (depending on chemical and quantity)
Respiratory protection not required.

## Slide 51: UTRGV Policy for sandals and shorts
Close toed shoes and long pants are required AT ALL TIMES in UTPA Laboratories.
X
X

## Slide 52: Injection
Caused by improper handling of sharps (pointed tools) or working with open wounds.
  Solution: Handle sharp objects with care and cover wounds while working.
  Use Sharps
Circulatory System

## Slide 53: Ingestion

## Slide 54: Ingestion
Caused by eating, drinking, smoking, touching your mouth with contaminated hands, or storing foods near chemicals.

## Slide 55: Protecting Your Self from Ingestion Exposure
Caused by eating, drinking, smoking, touching your mouth with contaminated hands, or storing foods near chemicals.
  Solution: No food, candy, or drinks are allowed in these areas. Do not eat or drink in the laboratory. Do not apply lip products in the laboratory.
  Wash hands thoroughly after you are finished working in the laboratory.

## Slide 56: Summary Protecting Yourself
Inhalation | Engineering controls , Ventilation Fume hood Respirator , Administrative Controls, Adequate
Ingestion | No Eating and Drinking in the Laboratory Housekeeping
Absorption | Cover exposed skin. Eye protection , Gloves; Masks. Close toed shoes; Long pants

## Slide 58: A thing about gloves
Gloves must be worn to protect hands from exposure to hazardous materials.
Glove selection should be based on an appropriate risk assessment. Review SDS Sheet
Alternatives to latex gloves should be available.
Change gloves when contaminated, glove integrity is compromised, or when otherwise necessary.
Remove gloves and wash hands when work with hazardous materials has been completed and before leaving the laboratory.
Do not wash or reuse disposable gloves. Dispose of used gloves with other contaminated laboratory waste. Hand washing protocols must be rigorously followed.

## Slide 59: Injection

## Slide 61: Protecting Yourself from Injection Exposure
Place sharps container in vicinity of where you are working
Dispose of sharps into sharps container free of charge
Sharps are considered medical waste

## Slide 62: American Chemical Society - Nanoparticles

## Slide 63: Laboratory Safety Guidelines for Using Nano-Materials (1)
LAB SAFETY GUIDELINES FOR HANDLING NANOMATERIALS
Use good general laboratory safety practices as found in your chemical hygiene plan. Wear gloves, lab coats, safety glasses, face shields, closed-toed shoes as needed.
Be sure to consider the hazards of precursor materials in evaluating process hazards.
Avoid skin contact with nanoparticles or nanoparticle-containing solutions by using appropriate personal protective equipment. Do not handle nanoparticles with your bare skin.
If it is necessary to handle nanoparticle powders outside of a HEPA-filtered powered-exhaust laminar flow hood, wear appropriate respiratory protection. The appropriate respirator should be selected based on professional consultation.
(1) American Chemical Society

## Slide 64: Recommendations (cont.)
Use fume exhaust hoods to expel fumes from tube furnaces or chemical reaction vessels.
Dispose of and transport waste nanoparticles according to hazardous chemical waste guidelines.
Vacuum cleaners used to clean up nanoparticles should be tested, HEPA-filtered units.
Equipment previously used to manufacture or handle nanoparticles should be evaluated for potential contamination prior to disposal or reuse for another purpose.
Lab equipment and exhaust systems should also be evaluated prior to removal, remodeling, or repair.
Given the differing synthetic methods and experimental goals, no blanket recommendation can be made regarding aerosol emissions controls. This should be evaluated on a case by case basis.
Consideration should be given to the high reactivity of some nanopowders materials with regard to potential fire and explosion hazards.

## Slide 65: Gas cylinders
Never use without formal training
Minimise the number in a laboratory
  Store externally whenever possible
Cylinders are heavy and can do serious damage to you if they fall
  Ensure that they are chained when in use
  Move only with a cylinder trolley
Use regulators & control equipment suitable for the gas concerned
Consider the consequences if your cylinder leaks

## Slide 66: Chemical Segregation
Distance and Barrier
Store chemicals according to hazard , not in alphabetical order (Alphabetize within categories)
Store acids, bases, flammables, oxidizers, etc. in separate locations
Flammables should be stored in flammable cabinets &/or explosion-proof refrigerators - not in regular refrigerators!

## Slide 67: Chemical Segregation

## Slide 68: Electrical Safety
Hot Plate
  Keep away from flammables/combustibles.
Bunsen Burner
  Tube must be free of defects.
  Keep away from flammables/combustibles.
Gas Cylinder
  Must be secured with strap to prevent tipping.
Vacuum pump
  Keep away from flammables/combustibles.
Electrical Cords
  Must be in good condition.
    Insulation is not worn, split or frayed.
    Plug is not separated from cord.
    Cord is not pinched in any way.
Electrical Panel
  If present, must remain unobstructed.
  Requires 3 ft. of clearance.
Extension cords may not be used as permanent wiring.
Power strips may not be connected in series.
(Daisy-chained.)

## Slide 69: Engineering Controls - Barriers
Storage Cabinets

## Slide 70: Storage

## Slide 71
Administrative Controls

## Slide 72: Door Placards

## Slide 73: Proper waste and chemical management: Labeling
Incorrect
Correct

## Slide 74: Proper Waste and Chemical Management: Storage
Incorrect
correct

## Slide 75: Regulated Waste Disposal

## Slide 76: Chemical Waste Disposal
Drain disposal is prohibited
Storage in lab
  Stored in compatible container
  Segregated from non-compatible wastes
  Closed at all times
  Descriptive name with the words “waste “
To dispose
  Filled containers should be removed from the laboratory within 72 hours
    Place date container is full on label
    Label
    Call EHSRM or submit work order

## Slide 77: Chemical Waste Disposal (cont)
Laboratory Supervisors including teaching assistants are responsible for ensuring compliance with TCEQ rules and regulations regarding waste disposal .

## Slide 78: Storage
Cap must be on the container except when adding or removing waste.
  Ensure container is properly closed, and labeled.
Correct
Incorrect
Incorrect

## Slide 79: Empty Containers:
Containers Containing Acutely Hazardous Chemicals must be Triple Rinsed to be considered empty.
Not on the list of acutely hazardous waste, the emptied container can be air-dried in a ventilated area (chemical fume hood) without triple rinsing.
Compressed Gas Cylinders and Aerosol Cans
Email waste@utrgv.edu for collection.

## Slide 80: Emergency Response

## Slide 81: Major Laboratory Accidents 1 of 3
1997 – Dartmouth accidental poisoning
  Professor Karen Wetterhahn followed MSDS guidelines for handling dimethyl mercury. However, the latex gloves she wore at the time of her exposure proved to be an insufficient barrier to her skin.
  While transferring dimethyl mercury with a mechanical pipette, 1-2 drops landed on her gloved hand. She didn’t consider the spill to be significant enough to report at the time. 5 month after her exposure she began to show serious neurological symptoms and was then treated for heavy metal poisoning.
  Karen became unresponsive 3 weeks into her treatment and died 10 months after the accident.

## Slide 82: Major Laboratory Accidents 2 of 3
2008 – University of California, Los Angeles fire
23-year-old staff research assistant Sheharbano (Sheri) Sangji was severely burned when air-sensitive chemicals burst into flames and ignited her clothing. And dies 18 days after the fire
Working in a fumehood, Sangji was drawing 50mL of tert-Butyllithium using a 60mL plastic syringe when for no known reason the plunger came out of the barrel.
An open flask of hexane, not part of her experiment, was knocked over. The tBuLi ignited and the solvent caught fire along with her clothes.
She was wearing nitrile gloves, no lab coat, and no one remembers if she had on eye protection.
Failed to use the safety shower

## Slide 83: If you incur an Injury
All injuries/chemical exposures must be reported
  Employees – Get immediate attention
    File a First Report of Injury via the EHSRM
  Students – Go directly to Health Services
Additionally, any conditions that make you feel unsafe must also be reported to 665-7256.
  You almost had an accident. (Near miss.)
  You observed someone else almost have an accident.
  Something is damaged or malfunctioning.
  Equipment/substances are being used incorrectly.
    Ex. Insufficient ventilation, no PPE, unsafe handling
  Not enough information/instructions were given on a subject and you do not feel confident in the laboratory.
  The work area’s cleanliness is not being maintained.
    Ex. Slip hazards or accumulation of hazardous wastes

## Slide 84: Chemical Spills
Assess the hazard.
Get help and seal off the area.
If the chemical has contacted anyone's skin, get that person to water immediately and wash the affected area.
Cover liquid spills with Spill Mix until all liquid is absorbed OR contact EHSRM to clean up the spill.
As necessary, protect yourself from fumes or contact with the chemical. Use appropriate PPE.
  Caution: Beware of odorless gases or olfactory fatigue.
Scoop the residue into a plastic pail.
Place the pail in a fume hood and report to EHSRM for disposal.
Major chemical spills and mercury spills are emergencies. Do not attempt to clean the area. Evacuate the affected area immediately.

## Slide 85: Chemical Spill

## Slide 86: Chemical Exposures
Chemicals on Skin
  Rinse for a minimum of 15 minutes at nearest safety shower.
  Remove contaminated clothing and jewelry.
Chemicals in Eyes
  Rinse for a minimum of 15 minutes at nearest eye wash.
  Keep eyelids open with fingers and thumbs.
  Remove contacts (do not reuse).
Chemical Inhalation
  Close the container, increase ventilation, move to fresh air.
Ingestions of Chemicals
  Do not induce vomiting unless instructed by a health care professional to do so.
Injection of Chemicals
  Wash the area with soap and water.
Inform emergency personnel of chemicals involved in the accident.

## Slide 87: Fires
Before
  Locate nearest fire extinguisher
  Locate nearest pull station
  Make sure all exits are clear
Do not attempt to fight a fire unless…
  you are trained to use a fire extinguisher.
  the fire is smaller than a standard trash can.
  Make sure you are between the fire and the exit.
If the fire is large and spreading…
  Activate the fire alarm (pull station) to alert other building occupants. Yell Fire; Fire !
  Close the door on your way out to contain the fire.
  Evacuate the building as soon as possible. Do not use the elevators.
    Do not re-enter the building.
  Call the University Police when it is safe to do so.

## Slide 88: Putting Out a Fire (PASS technique)

## Slide 89: Security
Areas containing chemicals must be Locked or under 100% surveillance at all times
Suspicious activity? Report immediately to UT Police (911)
Chemicals cannot be removed from campus without authorization